## Slide 1: Star-ccm+ training marine simulation cases
Enrico di Capua

## Slide 3: overview
STAR-CCM+
Case 1 – Hydrodynamic Performance
Case 2 – External Aerodynamics
Case 3 – Hydrofoil Design Exploration
Case 4 – Self-Propulsion
Conclusions
Objective: CFD training using Siemens STAR-CCM+
AGENDA

## Slide 4: What is STAR-ccm+ ?
A multiphysics Computational Fluid Dynamics (CFD) software by Siemens
Provides simulation of fluid flow, heat transfer, and solid mechanics
Handles complex geometries and realistic operating conditions
Used by leading companies to accelerate innovation

## Slide 5: CASE 1 hydrodynamic performance

## Slide 6: Key models
boat
Wave properties
Velocity: 20 knots
Mass: 2500 Kg
Dimensions: 5.6m x 1.8m x 0.6m
Oblique waves at 45 degrees onset to the boat
Wave height: 0.5m
Water depth: 100m
Wave period: 4s
The simulation was carried out to assess hull safety and comfort by verifying that wave slamming does not generate vertical accelerations above 1 g.
Purpose

## Slide 7: procedureS
The hull geometry was imported and positioned in oblique waves at 45°.
An overset mesh with Adaptive Mesh Refinement (AMR) was applied to capture the free surface motion
6DOF model enabled realistic hull motion (roll, pitch, heave).

## Slide 8: RESULTS
The boat experienced moderate roll (±3.8°), pitch (–12.5° to +0.2°), and a maximum heave of 0.5 m
The peak vertical acceleration was 0.58 g, remaining safely below the 1 g limit

## Slide 9: CASE 2 external aerodynamics

## Slide 10: Key models
boat
Wind
conditions
Dimensions: 200m x 35m x 55m
Wind speed: 10mph
Wind angle: 15 deg
The simulation aimed to ensure that the velocity in the vertical direction on the rear deck of the vessel did not exceed +/- 1.80 m/s
Purpose

## Slide 11: procedures
External flow domain created with refined boundary layer mesh
Steady-state CFD model applied to capture pressure and velocity distribution
Post-processing focused on drag coefficient and flow visualization

## Slide 12: RESULTS
Minimal fluctuation therefore the simulation is stable and converged
The maximum vertical velocity has converged to 1.78m/s
The entire rear deck of the MRV is within the safety margin of 1.80m/s in the vertical

## Slide 13: CASE 3 hydrofoil design exploration

## Slide 14: Key models
Hydrofoil shape
Design and boundary
Thickness: 0.19 m
Chord length: 1 m
Constant angle of attack: 0 deg
Modifying 2 points on the hydrofoil profile
Water velocity: 10 m/s
Angle of attack: 0 deg
The simulation assessed hydrofoil performance to balance lift and drag for efficient hydrodynamic design. Objective:
Lift Coefficient >= 0.3
Minimize Drag Coefficient
Purpose

## Slide 15: procedures
Hydrofoil geometry modeled under realistic flow conditions
Section planes and pressure contour visualizations created
Parametric study performed to explore performance variations

## Slide 16: RESULTS
If we take a look at our starting hydrofoil, Design 1:
Cdx100 = 0.8595
Cl = 0.3869
In comparison our best hydrofoil design, Design 17:
Cdx100 = 0.8290
Cl = 0.3111
This optimization has reduced drag 3.6% while keeping a minimum Cl of 0.3 in just 25 iterations.

## Slide 17: CASE 4 self propulsion

## Slide 18: Key models
ship
conditions
Dimensions: 150m x 31m x 23m
Air Temperature: 26.5C
Type of water: Sea
Sea density: 1023 kg/m 3
Ship speeds: 9.3, 11.6, 13 knots
The simulation investigated coupled hull–propeller interaction to analyze propulsion efficiency
Purpose

## Slide 19: procedures
Propeller modeled using an overset mesh to capture rotating motion
Coupled CFD simulation performed with hull and propulsion system

## Slide 20: RESULTS
Thrust curves demonstrated propeller effectiveness across operating points
CFD analysis confirmed reliable performance for integrated hull–propeller system.

## Slide 21: conclusions
Completed four marine CFD simulations using Siemens STAR-CCM+.
Each case explored a different aspect of marine design: hydrodynamics, aerodynamics, hydrofoil performance, and self-propulsion
Gained hands-on experience in:
Generating overset and adaptive meshes
Applying 6DOF models and monitoring hull motion
Post-processing results and extracting performance insights
Developed a solid understanding of CFD workflows and marine engineering analysis, enhancing technical and visualization skills for future projects.

## Slide 22: THANK YOU
Enrico di Capua - enricodicapua6@gmail.com
www.linkedin.com/in/enrico-di-capua
https://bit.ly/portfolio-enrico-di-capua